## Slide 1: PIQ: Persistent Interactive Queries for Network Security Analytics
ACM SDN-NFV Security ’19, March 27th 2019
Oliver Michel
John Sonchack
Eric Keller
Jonathan M. Smith
Notes: interactive and retroactive network monitoring queries for security analytics
  joint work with John Sonchack and Jonathan Smith from the University of Pennsylvania
  and Eric Keller from the University of Colorado Boulder

## Slide 2: Network Monitoring is important
Persistent Interactive Queries for Network Security Analytics | Oliver Michel
Security issues
Performance issues
Equipment failure
Misconfiguration
Notes: continuously monitoring the network is an important task
  detecting security issues — attacks
  debug performance issues: TCP incast, high queueing latency
  detect failures
  detect misconfiguration: load imbalance, routing loops, packet drops

## Slide 3: Today’s networks are larger and more complex than ever before
Persistent Interactive Queries for Network Security Analytics | Oliver Michel
Notes: especially true today
  handling variety of services
  complex management abstractions, e.g., network virtualization

## Slide 4: Today’s networks are larger and more complex than ever before
[Cisco Visual Networking Index 2017]
Persistent Interactive Queries for Network Security Analytics | Oliver Michel
Chart: Global IP Traffic Forecast
| 2015 | 2016 | 2017 | 2018 | 2019 | 2020
Region 1 | 72.5 | 88.7 | 108.5 | 132.1 | 160.6 | 194.4
Notes: on top of that: network traffic rapidly growing
  Cisco predicts IP traffic to grow 20% each year

## Slide 5: Network Threats grow rapidly
Chart: Total Ransomware Samples
| Q4 2015 | Q12016 | Q2 2016 | Q3 2016 | Q4 2016 | Q1 2017 | Q2 2017 | Q3 2017
 | 4.4 | 6 | 7.8 | 8.4 | 8.9 | 9.5 | 10.8 | 12.1
[McAfee Labs Thread Report Dec. 2017]
Persistent Interactive Queries for Network Security Analytics | Oliver Michel
Notes: at same time: more threats
  e.g., # of collected ransomware samples by McAfee doubled since 2015

## Slide 6: Passive Monitoring
Persistent Interactive Queries for Network Security Analytics | Oliver Michel
Telemetry
Analytics
[UnivMon, SIGCOMM ’16]
[Marple, SIGCOMM ’17]
[*Flow, ATC ’18]
[NetQRE, SIGCOMM ’17]
[Jetstream, HotCloud '18]
[Sonata, SIGCOMM ’18]
Notes: introduction of new programmable switches, seen a lot of work focusing on network monitoring
passive monitoring/record-based: export records of actual traffic and then compute statistics
  as opposed to polling SNMP
  architecture generally divided into two planes
  telemetry plane: implemented through programmable switches
    extract packet level information, generate records for analysis
  analytics plane: often using stream processing
    analytics in software
  examples

## Slide 7: Use in Practice
Persistent Interactive Queries for Network Security Analytics | Oliver Michel
[ip.src == 10.12.13.14] pkt rate > 10,000/s
[ip.src == 10.12.13.14] pkt rate > 10,000/s
[ip.dst == 10.12.13.14] tcp out-of-order > 1000/s
[ip.src == 10.12.13.14] pkt rate > 10,000/s
[ip.dst == 10.12.13.14] tcp out-of-order > 1000/s
[ip.src == 239.232.230.2] signature consistent with portscan
[ip.src == 10.12.13.14] pkt rate > 10,000/s
[ip.dst == 10.12.13.14] tcp out-of-order > 1000/s
[ip.src == 239.232.230.2] signature consistent with portscan
[ip.src == 123.123/24] traffic from blacklisted subnet
[ip.src == 10.12.13.14] pkt rate > 10,000/s
[ip.dst == 10.12.13.14] tcp out-of-order > 1000/s
[ip.src == 239.232.230.2] signature consistent with portscan
[ip.src == 123.123/24] traffic from blacklisted subnet
[ip.dst == 234.2.3.99] connections to unknown destination
[ip.src == 10.12.13.14] pkt rate > 10,000/s
[ip.dst == 10.12.13.14] tcp out-of-order > 1000/s
[ip.src == 239.232.230.2] signature consistent with portscan
[ip.src == 123.123/24] traffic from blacklisted subnet
[ip.dst == 234.2.3.99] connections to unknown destination
[switch1 queue 23] queue occupancy > 500 for > 5 min
Notes: see how a deployment would look like from operator perspective
  PFE-enabled switch at edge of network, equipped with telemetry, exports to analytics plane
  analytics plane runs long-running queries to detect a baseline of anomalies, generates alerts
    examples: [⇥⇥⇥⇥⇥⇥]
  problem: important to know/detect but information is insufficient to debug

## Slide 8: Use in Practice
Persistent Interactive Queries for Network Security Analytics | Oliver Michel
[switch1 queue 23] queue occupancy > 500 for > 5 min
38df6e44
avg. occupancy 627
2018-11-28 15:23:12.023112
incident id: 38df6e44
Notes: at very least: more detailed information
  exact condition that triggered alert
  precise timestamp
  most importantly: some reference to the incident
    allow operator or secondary system to look at exact packets that caused the condition
    look at problem in detail, perform manual or detailed data analysis

## Slide 9: Retrospective Network Queries
“show me sample 38df6e44”
  traffic looks normal
“show me information about queue 23”
  queue is part of load balancing group
“what other queues are in that load balancing group?”
  queues 24, 25, and 26
“show me traffic in queues 24, 25, 26 at 2018-11-28 15:23:12.023112”
  only control traffic
Persistent Interactive Queries for Network Security Analytics | Oliver Michel
Is there a configuration problem or do we ‘just’ receive
more than usual traffic?
Problem with Hashing? Other queues in group disabled?
Notes: introduce retrospective queries: a queue had an unusually high queue occupancy
  question: is there ‘just’ a lot of traffic or is there an issue → security or performance
  sample id … look at sample, apply different filters, maybe a standard summary script
  more information about location of the incident … queue is part of load balancing group
  what other queues are in that group? 24, 25, 26
  look at traffic in those queues: see only control traffic, maybe generate histogram of packet distribution
conclusion: something is going on … hashing, misconfiguration etc. — with just a warning would not have been able to figure out the exact problem: applies to many phenomena, especially everything that is across flows and at longer time scales, say Slowloris attack

## Slide 10: Retrospective Network Queries
Persistent Interactive Queries for Network Security Analytics | Oliver Michel
Persistent
Interactive Queries
Database
Query Interface
Notes: how to implement a system with this capability
  title suggests: two components
  persistent: need some way to store data beyond the short aggregation windows of the high throughput analytics system
  query interface: interactively look at data, present the data in different forms depending on problem

## Slide 11: Retrospective Network Queries
Persistent Interactive Queries for Network Security Analytics | Oliver Michel
Storing Network Records
Injecting Records into a Database
Querying the Database
Notes: after motivating need: three aspects to highlight
  store records
  efficiently inject records
  query

## Slide 12: Grouped Packet Vectors
GPV
22.4.24.9
118.24.1.7
6
34323
22
1.0239
34
1.7865
12
2.3239
45
SYN
SYN,ACK
FIN
…
…
…
Packet Records
22.4.24.9
118.24.1.7
6
34323
22
22.4.24.9
118.24.1.7
6
34323
22
22.4.24.9
118.24.1.7
6
34323
22
1.0239
34
SYN
1.7865
12
SYN,ACK
2.3239
45
FIN
…
…
…
Flow Records
22.4.24.9
118.24.1.7
6
34323
22
1.0239
1.1000
3
91
per-packet header fields
meta data: e.g., queue depth, ingress/egress timestamps
Persistent Interactive Queries for Network Security Analytics | Oliver Michel
aggregation keys
packet features
aggregated features
[Sonchack et.al. *Flow, USENIX ATC 2019]
Notes: first record format: leverage our previous work
  record format that PFE can assemble send to CPU: grouped packet vectors
  look at extremes
  packet records: duplicated information, not flexible
  flow records: generally rely on aggregation but we need per-packet data
  middle ground: grouped packet vectors: flow records with per [⇥] packet information

## Slide 13: Grouped Packet Vectors
GPVs provide high compression while maintaining information richness
Chart: Compression of 1 hour CAIDA Internet Packet Trace
| Packet Records | GPV | Flow Records
GB | 72 | 9.4 | 2.3
Persistent Interactive Queries for Network Security Analytics | Oliver Michel
Notes: efficiency: 72GB CAIDA Internet packet trace (headers)
  9.4 GB GPV data with μs timestamps, per packet sizes, tcp flags — compression 7.7x
  2.3 GB of NetFlow — aggregated values

## Slide 14: Database Models
Persistent Interactive Queries for Network Security Analytics | Oliver Michel
NoSQL
Relational
Time-Series
optimized for time-series data
  append-heavy workloads
  grouping functionality based on time
  timestamps as primary keys for data
  relational or NoSQL
Notes: decided need a database: database systems generally come in two flavors
  relational: rely on rigid relational model: more traditional enterprise workloads
  noSQL: more big data applications, generally better scalability, but less powerful ecosystem and query interface
  not an entirely new category but more recent development: time-series optimized databases —slide
    network monitoring records are inherently append, organized by time, from that point only read
chose timescale, relational postgres-based time-series database system: reasons why later

## Slide 15: Storing Network Records
Persistent Interactive Queries for Network Security Analytics | Oliver Michel
Notes: GPV for storage, can be associated with a sample
  packet records are separate relation
fields in detail: pkt_count, byte_count in gpv (duplication)
allows to after just delete pkt records, most queries still work, just don’t have per packet data anymore
most queries on gpv relation with join on gpv, requires relational model and SQL
  with other time series DBs not easily possible

## Slide 16: Storing Network Records
Persistent Interactive Queries for Network Security Analytics | Oliver Michel
Notes: measured the table size in timescale: grows linearly with record count
  pkt vs. gpv header record count ratio dependent on cache configuration
  between pkt and gpv at least 1 order of magnitude difference
  1 billion records 1TB + 20 - 90 GB

## Slide 17: Storing Network Records
Persistent Interactive Queries for Network Security Analytics | Oliver Michel
Notes: budget of 500B rows (roughly 500TB): caida packet traces had rate of around 330K/s -> 17 days of packet-level retention
  various policies for data retention on both packet and flow level are imaginable
  30-50K USD for such a storage system, disk array of 4 TB SATA disks

## Slide 18: Injecting Network Records
Persistent Interactive Queries for Network Security Analytics | Oliver Michel
INSERT INTO packets VALUES
  (‘2018-11-25 19:02:23.023219’,
  ‘123.213.123.4’, ‘213.11.23.23’, …)
1 auto buf = new char[h_len + 10000
2 * rec_len + t_len];
3
4 // 10000 times
5 pkt.write_to_pg_buf(buf, offset);
6
7 pg_conn.copy(“pkt”, buf, sizeof(buf));
Chart: INSERT
| 10K | 50K | 100K | 200K
INSERT | 0.016843 | 0.016745 | 0.016563 | 0.016035
Chart: COPY
| 10K | 50K | 100K | 200K
COPY | 0.30483 | 0.33831 | 0.35729 | 0.36222
Notes: next aspect: big challenge: inserting data
  two ways
    most common/widely known: INSERT: [⇥ ] data needs to be parsed ~15K records/s
    COPY (different types) binary: [⇥ ] ~300-360K records (>20x improvement)

## Slide 19: Injecting Network Records
Persistent Interactive Queries for Network Security Analytics | Oliver Michel
Notes: timescale vs. vanilla postgres insert:
  postgres performance declines faster with time
    mostly due to complex indices
      timescale indices are local to chunks, data ordered by timestamp…details in paper

## Slide 20: Querying Network Records
Persistent Interactive Queries for Network Security Analytics | Oliver Michel
SELECT time_bucket('1 seconds', ts_us) AS interval, SUM(pkt_count), SUM(byte_count)
    FROM gpv GROUP BY interval ORDER BY interval ASC
SELECT * FROM (gpv RIGHT JOIN pkt ON gpv.gpv_id = pkt.gpv_id)
WHERE gpv.ip_src << inet '60.70.0.0/16'
Notes: third: query interface
  use the power of SQL: aggregation, joins, and time series optimized helper functions
  generate a graph with 1s buckets
  all packets from that subnet

## Slide 21: Querying Network Records
Persistent Interactive Queries for Network Security Analytics | Oliver Michel
SELECT DISTINCT gpv.ip_src, gpv.ip_dst, gpv.ip_proto, gpv.tp_src, gpv.tp_dst
FROM (gpv RIGHT JOIN pkt ON gpv.gpv_id = pkt.gpv_id)
WHERE pkt.ingress_ts >= '2018-02-19 12:59:11.595’
AND pkt.ingress_ts < '2018-02-19 12:59:11.600'
AND pkt.queue_id = ’23’
SELECT pkt.queue_id, COUNT(pkt.queue_id)
FROM (gpv RIGHT JOIN pkt ON gpv.gpv_id = pkt.gpv_id)
WHERE gpv.ip_dst << inet ’53.231/16'
AND pkt.queue_id IN (23,24,25,26)
GROUP BY pkt.queue_id;
Notes: queue occupancy example in practice
  first query: packets in queue 23 at the time
  second query: histogram of packet counts over the four queues destined for a subnet
virtually unlimited query possibilities with instant results
allows for exploratory data analysis, iterative refinement

## Slide 22: Conclusion
Persistent Interactive Queries for Network Security Analytics | Oliver Michel
identify the need for retrospective network analytics
show using example queries how retrospective analytics
can be used to get better insight into what happened in
the network
implement a prototype application demonstrating
technical feasibility

## Slide 24
Backup Slides

## Slide 25: Example SQL Queries
SELECT ip_src, SUM(pkt_count)
FROM gpv WHERE ip_src << inet ’60.70.0.0/16’
    AND gpv.ts_us > now() - interval '1 hours’
    GROUP BY ip_src