## Slide 1: Programming Abstractions for AMD XNDATM NPUs
Low level of abstraction
High level of abstraction
IRON
Efficiency
Expressivity
Extensibility

## Slide 2: Agenda
Background
  AMD XDNATM NPUs
  IRON
Extensions to IRON
  Example program
Evaluation
Future Work

## Slide 3: Agenda
Background
  AMD XDNATM NPUs
  IRON
Extensions to IRON
  Example program
Evaluation
Future Work

## Slide 4: Background on AMD XNDATM NPUs

## Slide 5: Background on AMD XNDATM NPUs
The Neural Processing Unit (NPU)
…
Shim Tile
DMA
AIE Tile
Processor Core
L1
DMA
AIE Tile
Processor Core
L1
DMA
AIE Tile
Processor Core
L1
DMA
Memory Tile
L2
DMA
…
…
Shim Tile
DMA
AIE Tile
Processor Core
L1
DMA
AIE Tile
Processor Core
L1
DMA
AIE Tile
Processor Core
L1
DMA
Memory Tile
L2
DMA
…
Shim Tile
DMA
AIE Tile
Processor Core
L1
DMA
AIE Tile
Processor Core
L1
DMA
AIE Tile
Processor Core
L1
DMA
Memory Tile
L2
DMA
…
…
…
…
…
…
…
…
…
…
…
L3: External Memory

## Slide 6: Background on AMD XNDATM NPUs
…
Shim Tile
DMA
AIE Tile
Processor Core
L1
DMA
AIE Tile
Processor Core
L1
DMA
AIE Tile
Processor Core
L1
DMA
Memory Tile
L2
DMA
…
…
Shim Tile
DMA
AIE Tile
Processor Core
L1
DMA
AIE Tile
Processor Core
L1
DMA
AIE Tile
Processor Core
L1
DMA
Memory Tile
L2
DMA
…
Shim Tile
DMA
AIE Tile
Processor Core
L1
DMA
AIE Tile
Processor Core
L1
DMA
AIE Tile
Processor Core
L1
DMA
Memory Tile
L2
DMA
…
…
…
…
…
…
…
…
…
…
…
L3: External Memory
AI Engine
(AIE) array
Compute Tiles
Memory
(Mem) Tiles
Shim Tiles

## Slide 7: Background on AMD XNDATM NPUs
Spatially distributed compute and memory
Multi-level memory hierarchy
Explicitly scheduled, decoupled data movement
…
Shim Tile
DMA
AIE Tile
Processor Core
L1
DMA
AIE Tile
Processor Core
L1
DMA
AIE Tile
Processor Core
L1
DMA
Memory Tile
L2
DMA
…
…
Shim Tile
DMA
AIE Tile
Processor Core
L1
DMA
AIE Tile
Processor Core
L1
DMA
AIE Tile
Processor Core
L1
DMA
Memory Tile
L2
DMA
…
Shim Tile
DMA
AIE Tile
Processor Core
L1
DMA
AIE Tile
Processor Core
L1
DMA
AIE Tile
Processor Core
L1
DMA
Memory Tile
L2
DMA
…
…
…
…
…
…
…
…
…
…
…
L3: External Memory

## Slide 8: Background on AMD XNDATM NPUs
…
Shim Tile
DMA
AIE Tile
Processor Core
L1
DMA
AIE Tile
Processor Core
L1
DMA
AIE Tile
Processor Core
L1
DMA
Memory Tile
L2
DMA
…
…
Shim Tile
DMA
AIE Tile
Processor Core
L1
DMA
AIE Tile
Processor Core
L1
DMA
AIE Tile
Processor Core
L1
DMA
Memory Tile
L2
DMA
…
Shim Tile
DMA
AIE Tile
Processor Core
L1
DMA
AIE Tile
Processor Core
L1
DMA
AIE Tile
Processor Core
L1
DMA
Memory Tile
L2
DMA
…
…
…
…
…
…
…
…
…
…
…
L3: External Memory
Spatially distributed compute and memory
Multi-level memory hierarchy
Explicitly scheduled, decoupled data movement

## Slide 9: Background on AMD XNDATM NPUs
…
Shim Tile
DMA
AIE Tile
Processor Core
L1
DMA
AIE Tile
Processor Core
L1
DMA
AIE Tile
Processor Core
L1
DMA
Memory Tile
L2
DMA
…
…
Shim Tile
DMA
AIE Tile
Processor Core
L1
DMA
AIE Tile
Processor Core
L1
DMA
AIE Tile
Processor Core
L1
DMA
Memory Tile
L2
DMA
…
Shim Tile
DMA
AIE Tile
Processor Core
L1
DMA
AIE Tile
Processor Core
L1
DMA
AIE Tile
Processor Core
L1
DMA
Memory Tile
L2
DMA
…
…
…
…
…
…
…
…
…
…
…
L3: External Memory
Spatially distributed compute and memory
Multi-level memory hierarchy
Explicitly scheduled data movement

## Slide 10: Background on AMD XNDATM NPUs
…
Shim Tile
DMA
AIE Tile
Processor Core
L1
DMA
AIE Tile
Processor Core
L1
DMA
AIE Tile
Processor Core
L1
DMA
Memory Tile
L2
DMA
…
…
Shim Tile
DMA
AIE Tile
Processor Core
L1
DMA
AIE Tile
Processor Core
L1
DMA
AIE Tile
Processor Core
L1
DMA
Memory Tile
L2
DMA
…
Shim Tile
DMA
AIE Tile
Processor Core
L1
DMA
AIE Tile
Processor Core
L1
DMA
AIE Tile
Processor Core
L1
DMA
Memory Tile
L2
DMA
…
…
…
…
…
…
…
…
…
…
…
L3: External Memory
Spatially distributed compute and memory
Multi-level memory hierarchy
Explicitly scheduled data movement
Data Movement Accelerators (DMA)

## Slide 11: An NPU design needs…
Synchronization
Dataflow
Runtime operations

## Slide 12: An NPU design needs…
Synchronization
Dataflow
Runtime operations
Low level of abstraction
High level of abstraction

## Slide 13: An NPU design needs…
Synchronization
Dataflow
Runtime operations
Low level of abstraction
High level of abstraction
IRON
Exercise hardware features
Performance engineers
Research & education

## Slide 14: IRON: Open-source toolkit for AMD XDNATM NPUs
MLIR-AIE dialect
Python API
Example Programs
Programming Guide
Many details out of scope but described in paper or IRON programming guide.

## Slide 15: IRON Example: Matrix Scalar Add
Matrix
(Tensor)
Tile
(Sub-tensor)
+N
Out Data Movement
Element-wise scalar addition
In Data Movement
https://github.com/Xilinx/mlir-aie/tree/main/programming_examples/basic/matrix_scalar_add

## Slide 16
with mlir_mod_ctx() as ctx:
@device(AIEDevice.npu1_1col)
def device_body():
mty = np.ndarray[(MH, MW), np.dtype[np.int32]]
tty = np.ndarray[(TH, TW), np.dtype[np.int32]]
shm0 = tile(0, 0)
aie2 = tile(0, 2)
fi = object_fifo("in", shm0, aie2, 2, tty)
fo = object_fifo("out", aie2, shm0, 2, tty)
@core(aie2)
def core_body():
for _ in range_(sys.maxsize):
a = fi.acquire(ObjectFifoPort.Consume, 1)
b = fo.acquire(ObjectFifoPort.Produce, 1)
for i in range_(TH):
for j in range_(TW):
b[i, j] = a[i, j] + 1
fi.release(ObjectFifoPort.Consume, 1)
fo.release(ObjectFifoPort.Produce, 1)
@runtime_sequence(mty, mty)
def sequence(dati, dato):
in_task = shim_dma_single_bd_task(fi, dati,
sizes=[1, 1, TH, TW],
strides=[0, 0, MW, 1])
out_task = shim_dma_single_bd_task(fo, dato,
sizes=[1, 1, TH, TW],
strides=[0, 0, MW, 1],
issue_token=True)
dma_start_task(in_task, out_task)
dma_await_task(out_task)
dma_free_task(in_task)
print(ctx.module)

## Slide 17
with mlir_mod_ctx() as ctx:
@device(AIEDevice.npu1_1col)
def device_body():
mty = np.ndarray[(MH, MW), np.dtype[np.int32]]
tty = np.ndarray[(TH, TW), np.dtype[np.int32]]
shm0 = tile(0, 0)
aie2 = tile(0, 2)
fi = object_fifo("in", shm0, aie2, 2, tty)
fo = object_fifo("out", aie2, shm0, 2, tty)
@core(aie2)
def core_body():
for _ in range_(sys.maxsize):
a = fi.acquire(ObjectFifoPort.Consume, 1)
b = fo.acquire(ObjectFifoPort.Produce, 1)
for i in range_(TH):
for j in range_(TW):
b[i, j] = a[i, j] + 1
fi.release(ObjectFifoPort.Consume, 1)
fo.release(ObjectFifoPort.Produce, 1)
@runtime_sequence(mty, mty)
def sequence(dati, dato):
in_task = shim_dma_single_bd_task(fi, dati,
sizes=[1, 1, TH, TW],
strides=[0, 0, MW, 1])
out_task = shim_dma_single_bd_task(fo, dato,
sizes=[1, 1, TH, TW],
strides=[0, 0, MW, 1],
issue_token=True)
dma_start_task(in_task, out_task)
dma_await_task(out_task)
dma_free_task(in_task)
print(ctx.module)
Types and Resources

## Slide 18
with mlir_mod_ctx() as ctx:
@device(AIEDevice.npu1_1col)
def device_body():
mty = np.ndarray[(MH, MW), np.dtype[np.int32]]
tty = np.ndarray[(TH, TW), np.dtype[np.int32]]
shm0 = tile(0, 0)
aie2 = tile(0, 2)
fi = object_fifo("in", shm0, aie2, 2, tty)
fo = object_fifo("out", aie2, shm0, 2, tty)
@core(aie2)
def core_body():
for _ in range_(sys.maxsize):
a = fi.acquire(ObjectFifoPort.Consume, 1)
b = fo.acquire(ObjectFifoPort.Produce, 1)
for i in range_(TH):
for j in range_(TW):
b[i, j] = a[i, j] + 1
fi.release(ObjectFifoPort.Consume, 1)
fo.release(ObjectFifoPort.Produce, 1)
@runtime_sequence(mty, mty)
def sequence(dati, dato):
in_task = shim_dma_single_bd_task(fi, dati,
sizes=[1, 1, TH, TW],
strides=[0, 0, MW, 1])
out_task = shim_dma_single_bd_task(fo, dato,
sizes=[1, 1, TH, TW],
strides=[0, 0, MW, 1],
issue_token=True)
dma_start_task(in_task, out_task)
dma_await_task(out_task)
dma_free_task(in_task)
print(ctx.module)
Dataflow with ObjectFIFOs
Name, Source, Dest., Depth, Type

## Slide 19
with mlir_mod_ctx() as ctx:
@device(AIEDevice.npu1_1col)
def device_body():
mty = np.ndarray[(MH, MW), np.dtype[np.int32]]
tty = np.ndarray[(TH, TW), np.dtype[np.int32]]
shm0 = tile(0, 0)
aie2 = tile(0, 2)
fi = object_fifo("in", shm0, aie2, 2, tty)
fo = object_fifo("out", aie2, shm0, 2, tty)
@core(aie2)
def core_body():
for _ in range_(sys.maxsize):
a = fi.acquire(ObjectFifoPort.Consume, 1)
b = fo.acquire(ObjectFifoPort.Produce, 1)
for i in range_(TH):
for j in range_(TW):
b[i, j] = a[i, j] + 1
fi.release(ObjectFifoPort.Consume, 1)
fo.release(ObjectFifoPort.Produce, 1)
@runtime_sequence(mty, mty)
def sequence(dati, dato):
in_task = shim_dma_single_bd_task(fi, dati,
sizes=[1, 1, TH, TW],
strides=[0, 0, MW, 1])
out_task = shim_dma_single_bd_task(fo, dato,
sizes=[1, 1, TH, TW],
strides=[0, 0, MW, 1],
issue_token=True)
dma_start_task(in_task, out_task)
dma_await_task(out_task)
dma_free_task(in_task)
print(ctx.module)
Per-AIE core program
Dataflow + Kernel

## Slide 20
with mlir_mod_ctx() as ctx:
@device(AIEDevice.npu1_1col)
def device_body():
mty = np.ndarray[(MH, MW), np.dtype[np.int32]]
tty = np.ndarray[(TH, TW), np.dtype[np.int32]]
shm0 = tile(0, 0)
aie2 = tile(0, 2)
fi = object_fifo("in", shm0, aie2, 2, tty)
fo = object_fifo("out", aie2, shm0, 2, tty)
@core(aie2)
def core_body():
for _ in range_(sys.maxsize):
a = fi.acquire(ObjectFifoPort.Consume, 1)
b = fo.acquire(ObjectFifoPort.Produce, 1)
for i in range_(TH):
for j in range_(TW):
b[i, j] = a[i, j] + 1
fi.release(ObjectFifoPort.Consume, 1)
fo.release(ObjectFifoPort.Produce, 1)
@runtime_sequence(mty, mty)
def sequence(dati, dato):
in_task = shim_dma_single_bd_task(fi, dati,
sizes=[1, 1, TH, TW],
strides=[0, 0, MW, 1])
out_task = shim_dma_single_bd_task(fo, dato,
sizes=[1, 1, TH, TW],
strides=[0, 0, MW, 1],
issue_token=True)
dma_start_task(in_task, out_task)
dma_await_task(out_task)
dma_free_task(in_task)
print(ctx.module)
Input data
Output data

## Slide 21
with mlir_mod_ctx() as ctx:
@device(AIEDevice.npu1_1col)
def device_body():
mty = np.ndarray[(MH, MW), np.dtype[np.int32]]
tty = np.ndarray[(TH, TW), np.dtype[np.int32]]
shm0 = tile(0, 0)
aie2 = tile(0, 2)
fi = object_fifo("in", shm0, aie2, 2, tty)
fo = object_fifo("out", aie2, shm0, 2, tty)
@core(aie2)
def core_body():
for _ in range_(sys.maxsize):
a = fi.acquire(ObjectFifoPort.Consume, 1)
b = fo.acquire(ObjectFifoPort.Produce, 1)
for i in range_(TH):
for j in range_(TW):
b[i, j] = a[i, j] + 1
fi.release(ObjectFifoPort.Consume, 1)
fo.release(ObjectFifoPort.Produce, 1)
@runtime_sequence(mty, mty)
def sequence(dati, dato):
in_task = shim_dma_single_bd_task(fi, dati,
sizes=[1, 1, TH, TW],
strides=[0, 0, MW, 1])
out_task = shim_dma_single_bd_task(fo, dato,
sizes=[1, 1, TH, TW],
strides=[0, 0, MW, 1],
issue_token=True)
dma_start_task(in_task, out_task)
dma_await_task(out_task)
dma_free_task(in_task)
print(ctx.module)
Tile
(Sub-tensor)
Tile Width (TW)
Tile
Height
(TH)
Matrix Width (MW)
Matrix
Height
(MH)

## Slide 22
with mlir_mod_ctx() as ctx:
@device(AIEDevice.npu1_1col)
def device_body():
mty = np.ndarray[(MH, MW), np.dtype[np.int32]]
tty = np.ndarray[(TH, TW), np.dtype[np.int32]]
shm0 = tile(0, 0)
aie2 = tile(0, 2)
fi = object_fifo("in", shm0, aie2, 2, tty)
fo = object_fifo("out", aie2, shm0, 2, tty)
@core(aie2)
def core_body():
for _ in range_(sys.maxsize):
a = fi.acquire(ObjectFifoPort.Consume, 1)
b = fo.acquire(ObjectFifoPort.Produce, 1)
for i in range_(TH):
for j in range_(TW):
b[i, j] = a[i, j] + 1
fi.release(ObjectFifoPort.Consume, 1)
fo.release(ObjectFifoPort.Produce, 1)
@runtime_sequence(mty, mty)
def sequence(dati, dato):
in_task = shim_dma_single_bd_task(fi, dati,
sizes=[1, 1, TH, TW],
strides=[0, 0, MW, 1])
out_task = shim_dma_single_bd_task(fo, dato,
sizes=[1, 1, TH, TW],
strides=[0, 0, MW, 1],
issue_token=True)
dma_start_task(in_task, out_task)
dma_await_task(out_task)
dma_free_task(in_task)
print(ctx.module)
Recall, an NPU design needs…
Synchronization
Dataflow
Runtime operations

## Slide 23
with mlir_mod_ctx() as ctx:
@device(AIEDevice.npu1_1col)
def device_body():
mty = np.ndarray[(MH, MW), np.dtype[np.int32]]
tty = np.ndarray[(TH, TW), np.dtype[np.int32]]
shm0 = tile(0, 0)
aie2 = tile(0, 2)
fi = object_fifo("in", shm0, aie2, 2, tty)
fo = object_fifo("out", aie2, shm0, 2, tty)
@core(aie2)
def core_body():
for _ in range_(sys.maxsize):
a = fi.acquire(ObjectFifoPort.Consume, 1)
b = fo.acquire(ObjectFifoPort.Produce, 1)
for i in range_(TH):
for j in range_(TW):
b[i, j] = a[i, j] + 1
fi.release(ObjectFifoPort.Consume, 1)
fo.release(ObjectFifoPort.Produce, 1)
@runtime_sequence(mty, mty)
def sequence(dati, dato):
in_task = shim_dma_single_bd_task(fi, dati,
sizes=[1, 1, TH, TW],
strides=[0, 0, MW, 1])
out_task = shim_dma_single_bd_task(fo, dato,
sizes=[1, 1, TH, TW],
strides=[0, 0, MW, 1],
issue_token=True)
dma_start_task(in_task, out_task)
dma_await_task(out_task)
dma_free_task(in_task)
print(ctx.module)
Recall, an NPU design needs…
Synchronization
Dataflow
Runtime operations

## Slide 24
with mlir_mod_ctx() as ctx:
@device(AIEDevice.npu1_1col)
def device_body():
mty = np.ndarray[(MH, MW), np.dtype[np.int32]]
tty = np.ndarray[(TH, TW), np.dtype[np.int32]]
shm0 = tile(0, 0)
aie2 = tile(0, 2)
fi = object_fifo("in", shm0, aie2, 2, tty)
fo = object_fifo("out", aie2, shm0, 2, tty)
@core(aie2)
def core_body():
for _ in range_(sys.maxsize):
a = fi.acquire(ObjectFifoPort.Consume, 1)
b = fo.acquire(ObjectFifoPort.Produce, 1)
for i in range_(TH):
for j in range_(TW):
b[i, j] = a[i, j] + 1
fi.release(ObjectFifoPort.Consume, 1)
fo.release(ObjectFifoPort.Produce, 1)
@runtime_sequence(mty, mty)
def sequence(dati, dato):
in_task = shim_dma_single_bd_task(fi, dati,
sizes=[1, 1, TH, TW],
strides=[0, 0, MW, 1])
out_task = shim_dma_single_bd_task(fo, dato,
sizes=[1, 1, TH, TW],
strides=[0, 0, MW, 1],
issue_token=True)
dma_start_task(in_task, out_task)
dma_await_task(out_task)
dma_free_task(in_task)
print(ctx.module)
Efficiency
Read, write, modify designs
Only provide detail in areas of interest
Expressivity
Do not compromise on designer’s explicit control of hardware
Extensibility
Custom tooling, reusable logic

## Slide 25
with mlir_mod_ctx() as ctx:
@device(AIEDevice.npu1_1col)
def device_body():
mty = np.ndarray[(MH, MW), np.dtype[np.int32]]
tty = np.ndarray[(TH, TW), np.dtype[np.int32]]
shm0 = tile(0, 0)
aie2 = tile(0, 2)
fi = object_fifo("in", shm0, aie2, 2, tty)
fo = object_fifo("out", aie2, shm0, 2, tty)
@core(aie2)
def core_body():
for _ in range_(sys.maxsize):
a = fi.acquire(ObjectFifoPort.Consume, 1)
b = fo.acquire(ObjectFifoPort.Produce, 1)
for i in range_(TH):
for j in range_(TW):
b[i, j] = a[i, j] + 1
fi.release(ObjectFifoPort.Consume, 1)
fo.release(ObjectFifoPort.Produce, 1)
@runtime_sequence(mty, mty)
def sequence(dati, dato):
in_task = shim_dma_single_bd_task(fi, dati,
sizes=[1, 1, TH, TW],
strides=[0, 0, MW, 1])
out_task = shim_dma_single_bd_task(fo, dato,
sizes=[1, 1, TH, TW],
strides=[0, 0, MW, 1],
issue_token=True)
dma_start_task(in_task, out_task)
dma_await_task(out_task)
dma_free_task(in_task)
print(ctx.module)
Efficiency
Read, write, modify designs
Only provide detail in areas of interest
Expressivity
Do not compromise on designer’s explicit control of hardware
Extensibility
Custom tooling, reusable logic

## Slide 26
with mlir_mod_ctx() as ctx:
@device(AIEDevice.npu1_1col)
def device_body():
mty = np.ndarray[(MH, MW), np.dtype[np.int32]]
tty = np.ndarray[(TH, TW), np.dtype[np.int32]]
shm0 = tile(0, 0)
aie2 = tile(0, 2)
fi = object_fifo("in", shm0, aie2, 2, tty)
fo = object_fifo("out", aie2, shm0, 2, tty)
@core(aie2)
def core_body():
for _ in range_(sys.maxsize):
a = fi.acquire(ObjectFifoPort.Consume, 1)
b = fo.acquire(ObjectFifoPort.Produce, 1)
for i in range_(TH):
for j in range_(TW):
b[i, j] = a[i, j] + 1
fi.release(ObjectFifoPort.Consume, 1)
fo.release(ObjectFifoPort.Produce, 1)
@runtime_sequence(mty, mty)
def sequence(dati, dato):
in_task = shim_dma_single_bd_task(fi, dati,
sizes=[1, 1, TH, TW],
strides=[0, 0, MW, 1])
out_task = shim_dma_single_bd_task(fo, dato,
sizes=[1, 1, TH, TW],
strides=[0, 0, MW, 1],
issue_token=True)
dma_start_task(in_task, out_task)
dma_await_task(out_task)
dma_free_task(in_task)
print(ctx.module)
Efficiency
Read, write, modify designs
Only provide detail in areas of interest
Expressivity
Do not compromise on designer’s explicit control of hardware
Extensibility
Custom tooling, reusable logic

## Slide 27
with mlir_mod_ctx() as ctx:
@device(AIEDevice.npu1_1col)
def device_body():
mty = np.ndarray[(MH, MW), np.dtype[np.int32]]
tty = np.ndarray[(TH, TW), np.dtype[np.int32]]
shm0 = tile(0, 0)
aie2 = tile(0, 2)
fi = object_fifo("in", shm0, aie2, 2, tty)
fo = object_fifo("out", aie2, shm0, 2, tty)
@core(aie2)
def core_body():
for _ in range_(sys.maxsize):
a = fi.acquire(ObjectFifoPort.Consume, 1)
b = fo.acquire(ObjectFifoPort.Produce, 1)
for i in range_(TH):
for j in range_(TW):
b[i, j] = a[i, j] + 1
fi.release(ObjectFifoPort.Consume, 1)
fo.release(ObjectFifoPort.Produce, 1)
@runtime_sequence(mty, mty)
def sequence(dati, dato):
in_task = shim_dma_single_bd_task(fi, dati,
sizes=[1, 1, TH, TW],
strides=[0, 0, MW, 1])
out_task = shim_dma_single_bd_task(fo, dato,
sizes=[1, 1, TH, TW],
strides=[0, 0, MW, 1],
issue_token=True)
dma_start_task(in_task, out_task)
dma_await_task(out_task)
dma_free_task(in_task)
print(ctx.module)
Efficiency
Read, write, modify designs
Only provide detail in areas of interest
Expressivity
Do not compromise on designer’s explicit control of hardware
Extensibility
Custom tooling, reusable logic

## Slide 28: Agenda
Background
  AMD XDNATM NPUs
  IRON
Extensions to IRON
  Example program
Evaluation
Future Work

## Slide 29: Extensions to IRON
Key Technique:
  Distance from MLIR
Enables:
  Refined constructs
  Defaults and extensions

## Slide 30: Distance from MLIR
fi = object_fifo("in", shm0, aie2, 2, tty)
MLIR
MLIR Python Bindings

## Slide 31: Distance from MLIR
fi = object_fifo("in", shm0, aie2, 2, tty)
MLIR
ObjectFifo(tty)
Extensions to IRON
MLIR Python Bindings
resolve()

## Slide 32: Refined Constructs
Program
Worker
Runtime
ObjectFIFO

## Slide 33: Refined Constructs
Program
Worker
Runtime
ObjectFIFO
With Extensions
mty = np.ndarray[(MH, MW), np.dtype[np.int32]]
tty = np.ndarray[(TH, TW), np.dtype[np.int32]]
fi = ObjectFifo(tty)
fo = ObjectFifo(tty)
def core_fn(of_in, of_out):
a = of_in.acquire(1)
b = of_out.acquire(1)
for i in range_(TH):
for j in range_(TW):
b[i, j] = a[i, j] + 1
of_in.release(1)
of_out.release(1)
my_worker = Worker(core_fn,
fn_args=[fi.cons(), fo.prod()])
tap = TensorTiler2D.simple_tiler(
(MH, MW), (TH, TW))[0]
rt = Runtime()
with rt.sequence(mty, mty) as (dati, dato):
rt.start(my_worker)
rt.fill(fi.prod(), dati, tap)
rt.drain(fo.cons(), dato, tap, wait=True)
print(Program(NPU1Col1(),rt).resolve_program(
SequentialPlacer()))

## Slide 34: Refined Constructs
Program
Worker
Runtime
ObjectFIFO
mty = np.ndarray[(MH, MW), np.dtype[np.int32]]
tty = np.ndarray[(TH, TW), np.dtype[np.int32]]
fi = ObjectFifo(tty)
fo = ObjectFifo(tty)
def core_fn(of_in, of_out):
a = of_in.acquire(1)
b = of_out.acquire(1)
for i in range_(TH):
for j in range_(TW):
b[i, j] = a[i, j] + 1
of_in.release(1)
of_out.release(1)
my_worker = Worker(core_fn,
fn_args=[fi.cons(), fo.prod()])
tap = TensorTiler2D.simple_tiler(
(MH, MW), (TH, TW))[0]
rt = Runtime()
with rt.sequence(mty, mty) as (dati, dato):
rt.start(my_worker)
rt.fill(fi.prod(), dati, tap)
rt.drain(fo.cons(), dato, tap, wait=True)
print(Program(NPU1Col1(),rt).resolve_program(
SequentialPlacer()))

## Slide 35: Refined Constructs
Program
Worker
Runtime
ObjectFIFO
mty = np.ndarray[(MH, MW), np.dtype[np.int32]]
tty = np.ndarray[(TH, TW), np.dtype[np.int32]]
fi = ObjectFifo(tty)
fo = ObjectFifo(tty)
def core_fn(of_in, of_out):
a = of_in.acquire(1)
b = of_out.acquire(1)
for i in range_(TH):
for j in range_(TW):
b[i, j] = a[i, j] + 1
of_in.release(1)
of_out.release(1)
my_worker = Worker(core_fn,
fn_args=[fi.cons(), fo.prod()])
tap = TensorTiler2D.simple_tiler(
(MH, MW), (TH, TW))[0]
rt = Runtime()
with rt.sequence(mty, mty) as (dati, dato):
rt.start(my_worker)
rt.fill(fi.prod(), dati, tap)
rt.drain(fo.cons(), dato, tap, wait=True)
print(Program(NPU1Col1(),rt).resolve_program(
SequentialPlacer()))

## Slide 36: Refined Constructs
Program
Worker
Runtime
ObjectFIFO
mty = np.ndarray[(MH, MW), np.dtype[np.int32]]
tty = np.ndarray[(TH, TW), np.dtype[np.int32]]
fi = ObjectFifo(tty)
fo = ObjectFifo(tty)
def core_fn(of_in, of_out):
a = of_in.acquire(1)
b = of_out.acquire(1)
for i in range_(TH):
for j in range_(TW):
b[i, j] = a[i, j] + 1
of_in.release(1)
of_out.release(1)
my_worker = Worker(core_fn,
fn_args=[fi.cons(), fo.prod()])
tap = TensorTiler2D.simple_tiler(
(MH, MW), (TH, TW))[0]
rt = Runtime()
with rt.sequence(mty, mty) as (dati, dato):
rt.start(my_worker)
rt.fill(fi.prod(), dati, tap)
rt.drain(fo.cons(), dato, tap, wait=True)
print(Program(NPU1Col1(),rt).resolve_program(
SequentialPlacer()))

## Slide 37: Refined Constructs
Program
Worker
Runtime
ObjectFIFO
mty = np.ndarray[(MH, MW), np.dtype[np.int32]]
tty = np.ndarray[(TH, TW), np.dtype[np.int32]]
fi = ObjectFifo(tty)
fo = ObjectFifo(tty)
def core_fn(of_in, of_out):
a = of_in.acquire(1)
b = of_out.acquire(1)
for i in range_(TH):
for j in range_(TW):
b[i, j] = a[i, j] + 1
of_in.release(1)
of_out.release(1)
my_worker = Worker(core_fn,
fn_args=[fi.cons(), fo.prod()])
tap = TensorTiler2D.simple_tiler(
(MH, MW), (TH, TW))[0]
rt = Runtime()
with rt.sequence(mty, mty) as (dati, dato):
rt.start(my_worker)
rt.fill(fi.prod(), dati, tap)
rt.drain(fo.cons(), dato, tap, wait=True)
print(Program(NPU1Col1(),rt).resolve_program(
SequentialPlacer()))

## Slide 38: Extensibility
Placement
On-the-fly Data Transformations

## Slide 39: Extensibility
Placement
On-the-fly Data Transformations
mty = np.ndarray[(MH, MW), np.dtype[np.int32]]
tty = np.ndarray[(TH, TW), np.dtype[np.int32]]
fi = ObjectFifo(tty)
fo = ObjectFifo(tty)
def core_fn(of_in, of_out):
a = of_in.acquire(1)
b = of_out.acquire(1)
for i in range_(TH):
for j in range_(TW):
b[i, j] = a[i, j] + 1
of_in.release(1)
of_out.release(1)
my_worker = Worker(core_fn,
fn_args=[fi.cons(), fo.prod()])
tap = TensorTiler2D.simple_tiler(
(MH, MW), (TH, TW))[0]
rt = Runtime()
with rt.sequence(mty, mty) as (dati, dato):
rt.start(my_worker)
rt.fill(fi.prod(), dati, tap)
rt.drain(fo.cons(), dato, tap, wait=True)
print(Program(NPU1Col1(),rt).resolve_program(
SequentialPlacer()))

## Slide 40: Extensibility
Placement
On-the-fly Data Transformations
  tap: Tensor Access Pattern
  tas: Tensor Access Sequence
mty = np.ndarray[(MH, MW), np.dtype[np.int32]]
tty = np.ndarray[(TH, TW), np.dtype[np.int32]]
fi = ObjectFifo(tty)
fo = ObjectFifo(tty)
def core_fn(of_in, of_out):
a = of_in.acquire(1)
b = of_out.acquire(1)
for i in range_(TH):
for j in range_(TW):
b[i, j] = a[i, j] + 1
of_in.release(1)
of_out.release(1)
my_worker = Worker(core_fn,
fn_args=[fi.cons(), fo.prod()])
tap = TensorTiler2D.simple_tiler(
(MH, MW), (TH, TW))[0]
rt = Runtime()
with rt.sequence(mty, mty) as (dati, dato):
rt.start(my_worker)
rt.fill(fi.prod(), dati, tap)
rt.drain(fo.cons(), dato, tap, wait=True)
print(Program(NPU1Col1(),rt).resolve_program(
SequentialPlacer()))
More information in paper!

## Slide 41: Agenda
Background
  AMD XDNATM NPUs
  IRON
Extensions to IRON
  Example program
Evaluation
Future Work

## Slide 42: 27 Sample designs
Evaluation Goals: Efficiency, Expressivity, Extensibility
Imperfect metrics, but representative of trends
See paper for more details

## Slide 43: Designer Efficiency – Decrease in single lines of code (SLOC)

## Slide 44: Designer Efficiency – Decreases in Halstead vocabulary (top) and effort (bottom)

## Slide 45: SequentialPlacer
24/27 examples
mty = np.ndarray[(MH, MW), np.dtype[np.int32]]
tty = np.ndarray[(TH, TW), np.dtype[np.int32]]
fi = ObjectFifo(tty)
fo = ObjectFifo(tty)
def core_fn(of_in, of_out):
a = of_in.acquire(1)
b = of_out.acquire(1)
for i in range_(TH):
for j in range_(TW):
b[i, j] = a[i, j] + 1
of_in.release(1)
of_out.release(1)
my_worker = Worker(core_fn,
fn_args=[fi.cons(), fo.prod()])
tap = TensorTiler2D.simple_tiler(
(MH, MW), (TH, TW))[0]
rt = Runtime()
with rt.sequence(mty, mty) as (dati, dato):
rt.start(my_worker)
rt.fill(fi.prod(), dati, tap)
rt.drain(fo.cons(), dato, tap, wait=True)
print(Program(NPU1Col1(),rt).resolve_program(
SequentialPlacer()))

## Slide 46: TensorTiler2D
5 designs
mty = np.ndarray[(MH, MW), np.dtype[np.int32]]
tty = np.ndarray[(TH, TW), np.dtype[np.int32]]
fi = ObjectFifo(tty)
fo = ObjectFifo(tty)
def core_fn(of_in, of_out):
a = of_in.acquire(1)
b = of_out.acquire(1)
for i in range_(TH):
for j in range_(TW):
b[i, j] = a[i, j] + 1
of_in.release(1)
of_out.release(1)
my_worker = Worker(core_fn,
fn_args=[fi.cons(), fo.prod()])
tap = TensorTiler2D.simple_tiler(
(MH, MW), (TH, TW))[0]
rt = Runtime()
with rt.sequence(mty, mty) as (dati, dato):
rt.start(my_worker)
rt.fill(fi.prod(), dati, tap)
rt.drain(fo.cons(), dato, tap, wait=True)
print(Program(NPU1Col1(),rt).resolve_program(
SequentialPlacer()))

## Slide 47: Matrix Multiplication Visualization of Runtime DMA Ops
https://github.com/Xilinx/mlir-aie/blob/main/programming_examples/basic/matrix_multiplication/whole_array/mat_mul_whole_array_visualization.ipynb
B Runtime DMA Pattern
C Runtime DMA Pattern
Note: Timing between animations is not coordinated
A Runtime DMA Pattern

## Slide 48: Agenda
Background
  AMD XDNATM NPUs
  IRON
Extensions to IRON
  Example program
Evaluation
Future Work

## Slide 49: Future Work
Extend further
Currently integrated and available!
Improvements:
1) Debugging, tracing
2) Data visualizations
3) …
Enable related works
ObjectFIFO analysis
Analyze similarities to other platforms
Support advanced designs

## Slide 50: Questions?
IRON (MLIR-AIE): https://github.com/Xilinx/mlir-aie
MLIR-AIE & IRON are a project many have contributed to: Thank you!

## Slide 51: Efficiency, Expressivity, and Extensibility in a Close-to-Metal NPU Programming Interface
Erika Hunhoff‡†, Joseph Melber∗, Kristof Denolf∗, Andra Bisca∗, Samuel Bayliss∗, Stephen Neuendorffer∗, Jeff Fifield∗, Jack Lo∗, Pranathi Vasireddy∗, Phil James-Roxby∗, Eric Keller†
∗AMD †University of Colorado at Boulder ‡Work performed at AMD

## Slide 52
with mlir_mod_ctx() as ctx:
@device(AIEDevice.npu1_1col)
def device_body():
mty = np.ndarray[(MH, MW), np.dtype[np.int32]]
tty = np.ndarray[(TH, TW), np.dtype[np.int32]]
shm0 = tile(0, 0)
aie2 = tile(0, 2)
fi = object_fifo("in", shm0, aie2, 2, tty)
fo = object_fifo("out", aie2, shm0, 2, tty)
@core(aie2)
def core_body():
for _ in range_(sys.maxsize):
a = fi.acquire(ObjectFifoPort.Consume, 1)
b = fo.acquire(ObjectFifoPort.Produce, 1)
for i in range_(TH):
for j in range_(TW):
b[i, j] = a[i, j] + 1
fi.release(ObjectFifoPort.Consume, 1)
fo.release(ObjectFifoPort.Produce, 1)
@runtime_sequence(mty, mty)
def sequence(dati, dato):
in_task = shim_dma_single_bd_task(fi, dati,
sizes=[1, 1, TH, TW],
strides=[0, 0, MW, 1])
out_task = shim_dma_single_bd_task(fo, dato,
sizes=[1, 1, TH, TW],
strides=[0, 0, MW, 1],
issue_token=True)
dma_start_task(in_task, out_task)
dma_await_task(out_task)
dma_free_task(in_task)
print(ctx.module)
Target device

## Slide 53
with mlir_mod_ctx() as ctx:
@device(AIEDevice.npu1_1col)
def device_body():
mty = np.ndarray[(MH, MW), np.dtype[np.int32]]
tty = np.ndarray[(TH, TW), np.dtype[np.int32]]
shm0 = tile(0, 0)
aie2 = tile(0, 2)
fi = object_fifo("in", shm0, aie2, 2, tty)
fo = object_fifo("out", aie2, shm0, 2, tty)
@core(aie2)
def core_body():
for _ in range_(sys.maxsize):
a = fi.acquire(ObjectFifoPort.Consume, 1)
b = fo.acquire(ObjectFifoPort.Produce, 1)
for i in range_(TH):
for j in range_(TW):
b[i, j] = a[i, j] + 1
fi.release(ObjectFifoPort.Consume, 1)
fo.release(ObjectFifoPort.Produce, 1)
@runtime_sequence(mty, mty)
def sequence(dati, dato):
in_task = shim_dma_single_bd_task(fi, dati,
sizes=[1, 1, TH, TW],
strides=[0, 0, MW, 1])
out_task = shim_dma_single_bd_task(fo, dato,
sizes=[1, 1, TH, TW],
strides=[0, 0, MW, 1],
issue_token=True)
dma_start_task(in_task, out_task)
dma_await_task(out_task)
dma_free_task(in_task)
print(ctx.module)

## Slide 54: Goals
Efficiency
Read, write, modify designs
Only provide detail in areas of interest
Expressivity
Do not compromise on designer’s explicit control of hardware
Extensibility
Custom tooling, reusable logic

## Slide 55: Tensor Access Pattern Tools: TensorTiler2D
from aie.helpers.taplib import TensorTiler2D
taps = TensorTiler2D.step_tiler(
(4, 8),
(1, 1),
tile_group_repeats=[2, 3],
tile_group_steps=[2, 2],
allow_partial=True)
1x1
1x1
1x1
1x1
1x1
1x1
x3
x2
Step 2
Step 2

## Slide 56: Tensor Access Pattern Tools: TensorTiler2D
from aie.helpers.taplib import TensorTiler2D
taps = TensorTiler2D.step_tiler(
(4, 8),
(1, 1),
tile_group_repeats=[2, 3],
tile_group_steps=[2, 2],
allow_partial=True)
taps.visualize()

## Slide 57: Tensor Access Pattern Tools: TensorTiler2D
from aie.helpers.taplib import TensorTiler2D
taps = TensorTiler2D.step_tiler(
(4, 8),
(1, 1),
tile_group_repeats=[2, 3],
tile_group_steps=[2, 2],
allow_partial=True)
anim = taps.animate()
# View in notebook
HTML(anim.to_jshtml())
# Save to file
anim.save("myfile.gif")